## Slide 1
Enterprise Network Design for Multi-National Company
Optimizing Connectivity and Security Across Egypt & Saudi Arabia

## Slide 2
Team
Abdelrahman Radwan
Abdelrahman Khaled
Mahmoud Safwat
Ahmed Mohamed Afifi
Mariam Dweidar

## Slide 3
Project Overview: Building a Resilient Network
This project outlines the robust network infrastructure for a multinational enterprise with significant operations in Egypt and Saudi Arabia. Our design focuses on seamless connectivity, high availability, and stringent security across all locations.
2
Headquarters
Strategic hubs in Egypt and Saudi Arabia.
4+
Branch Offices
Distributed across key regional cities.
15+
Network Devices
Routers, switches, firewalls, and APs.

## Slide 4
Network Architecture: A Holistic View
The proposed architecture integrates two primary Headquarters (HQ1 in Egypt, HQ2 in Saudi Arabia) and multiple branch offices. All sites will be interconnected via secure links, ensuring efficient data exchange and communication.
HQ1 & HQ2: Core network infrastructure, centralized services.
Branch Offices: Local network access with VPN connectivity to HQs.
VPN Tunnels: Encrypted communication channels between all sites.
Wireless Access: Secure Wi-Fi deployment for user mobility.

## Slide 5
Security Implementation: Protecting Critical Assets
Our security strategy is built upon the pillars of Confidentiality, Integrity, and Availability (CIA), employing multi-layered defenses to safeguard the enterprise network.
Confidentiality
Ensured through robust encryption (VPNs) and strict access controls.
Integrity
Maintained via checksums, digital signatures, and secure data handling protocols.
Availability
Guaranteed by redundant systems and proactive monitoring.
Further reinforced by advanced firewalls and AAA (Authentication, Authorization, Accounting) for user and device access management.

## Slide 6
High Availability: Ensuring Continuous Operation
Network uptime is paramount for multinational operations. Our design incorporates several mechanisms to eliminate single points of failure and ensure uninterrupted service.
VRRP (Virtual Router Redundancy Protocol)
Provides automatic failover for default gateways, ensuring network traffic continues even if a router fails.
Link Aggregation (Eth-Trunk)
Bundles multiple physical links into a single logical link, increasing bandwidth and providing link redundancy.
Dual WAN Connections
Utilizes two separate internet service providers or circuits to prevent outages due to a single ISP failure.

## Slide 7
Routing Protocols: Dynamic Path Selection
Efficient and scalable routing is achieved through a combination of industry-standard protocols, adapting to network changes dynamically.
OSPF (Open Shortest Path First): Interior Gateway Protocol (IGP) for rapid convergence within each HQ and branch network.
BGP (Border Gateway Protocol): Exterior Gateway Protocol (EGP) for robust routing between the two Headquarters and for internet connectivity..

## Slide 8
Network Services: Enhancing Performance and Management
A suite of essential network services is implemented to optimize performance, facilitate management, and support critical applications like VoIP.
SNMP (Simple Network Management Protocol)
For centralized monitoring and management of network devices.
NetStream
Provides detailed network traffic analysis and visibility.
QoS (Quality of Service)
Prioritizes critical traffic like VoIP to ensure optimal performance.
VoIP Support
Dedicated configurations to ensure high-quality voice communication.

## Slide 9
IP Addressing & VLAN Plan
A structured IP addressing scheme and VLAN segmentation are critical for network organization, security, and broadcast domain management.
Location/VLAN
IP Subnet
Purpose
VLAN ID
HQ1 - Data
10.0.1.0/24
General Data Traffic
10
HQ1 - Voice
10.0.2.0/24
VoIP Traffic
20
HQ2 - Data
10.0.11.0/24
General Data Traffic
110
HQ2 - Voice
10.0.12.0/24
VoIP Traffic
120
Branches - Data
10.0.X.0/24
Branch Data Traffic
100+X
Branches - Voice
10.0.Y.0/24
Branch VoIP Traffic
200+Y
DMZ
172.16.0.0/28
Public-facing Services
900
VPN Links
192.168.0.0/30
Inter-site VPN Tunnels
--

## Slide 10
Topology

## Slide 11
Learning Objectives & Technologies Used
Learning Objectives
HCIA (Huawei Certified ICT Associate) - DataCom: Foundational knowledge for enterprise networking.
HCIP (Huawei Certified ICT Professional) - DataCom: Advanced skills in planning, deploying, and troubleshooting complex networks.
Key Technologies Used
Huawei eNSP: Network simulation platform for design and testing.
Huawei AR Routers: Enterprise-grade access and aggregation routers.
Huawei CE Switches: CloudEngine series switches for high-performance data centers and campus networks.
Huawei USG Firewalls: Unified Security Gateways for comprehensive network protection.

## Slide 12
Summary & Benefits: A Future-Proof Network
This enterprise network design delivers a robust, secure, and highly available infrastructure tailored for the demands of a multinational company operating in Egypt and Saudi Arabia.
Scalability
Designed to effortlessly accommodate future growth and expansion of operations.
Security
Multi-layered defenses protect sensitive data and ensure business continuity.
Redundancy
Eliminates single points of failure, ensuring maximum uptime and reliability.
By adopting this design, the enterprise will achieve superior network performance, enhance operational efficiency, and significantly reduce potential downtime.